## Slide 1
Automatic Repeat Request
Latency Leaders
ARQ
Team Presentation
Members-
  Aniket
  Satyam
  Gurshaan
  Chaya
  Mukesh

## Slide 2
WHAT IS ARQ?
ARQ (Automatic Repeat Request) is a technique used to ensure the reliable delivery of data by retransmitting lost or corrupted packets.
In RLC ARQ, the sender waits for an acknowledgment (ACK) from the receiver for each transmitted data packet. If the acknowledgment is not received or a negative acknowledgment (NACK) is sent (indicating a loss or corruption), the packet is retransmitted.
Latency Leaders

## Slide 3
REAL-LIFE EXAMPLE
Latency Leaders

## Slide 4
Latency Leaders
Real-World Example: ARQ in RLC
📱 Imagine you are texting a friend, but due to a weak network, some words are missing.
You send: "Meet me at the coffee shop at 5 PM."
Your friend receives: "Meet me at the … shop at 5 PM."
Your friend replies: "I didn’t get the missing word. Send again!"
You resend: "coffee"
Your friend gets the full message.
Here, the missing part of the message (coffee) is resent instead of the entire message—just like Selective Repeat ARQ in RLC.

## Slide 5
WORKING OF RLC ARQ PROCEDURE
Latency Leaders

## Slide 6
The ARQ procedure consists of the following key steps:
  Transmission of Data: The sender (typically the mobile device or base station) transmits data packets (called RLC blocks or RLC SDUs) to the receiver (base station or mobile device).
  Acknowledgment: The receiver sends an acknowledgment (ACK) back to the sender after successfully receiving a packet. If the packet is not received correctly or if there is a loss, a negative acknowledgment (NACK) is sent.
  Retransmission of Lost Packets: If the sender does not receive an acknowledgment (or receives a NACK) for a specific packet, it will retransmit that packet. This retransmission can continue until the packet is successfully acknowledged, or a maximum number of retransmissions is reached.

## Slide 7
  Sequence Numbering: Each transmitted data packet is assigned a unique sequence number, allowing the receiver to determine the order of packets and detect lost packets.
  Buffering: The sender and receiver maintain buffers to temporarily store data. The receiver keeps track of successfully received packets and their order. The sender may also buffer packets that have been transmitted but not yet acknowledged, allowing for retransmissions when necessary.

## Slide 8
Latency Leaders
WORKING OF ARQ

## Slide 9
TYPES OF ARQ
Latency Leaders

## Slide 10
There are three main types of Automatic Repeat Request (ARQ) mechanisms used in data communication to ensure reliable transmission:
  Stop-and-Wait ARQ
  Go-Back-N ARQ
  Selective Repeat ARQ

## Slide 11
  How it Works:
    The sender transmits one data packet and waits for an acknowledgment (ACK) before sending the next packet.
    If an ACK is received, the sender transmits the next packet.
    If a Negative Acknowledgment (NACK) or no response is received (timeout occurs), the sender retransmits the same packet.
  Pros:
    Simple and easy to implement.
    Requires minimal memory as only one packet is in transmission at a time.
  Cons:
    Inefficient for high-latency networks because the sender has to wait before sending the next packet.
    Throughput is limited since only one packet is sent at a time.
  Use Cases:
    Low-speed and low-latency networks where simplicity is preferred over efficiency.
STOP-AND-WAIT ARQ

## Slide 12
Latency Leaders
SAMPLE IMPLEMENTATION OF STOP-N-WAIT ARQ

## Slide 13
How it Works:
  The sender can send multiple packets (up to a predefined window size) without waiting for an acknowledgment.
  If an error is detected (NACK received or timeout occurs), the sender retransmits the erroneous packet and all subsequent packets in sequence.
  Uses a sliding window mechanism to manage the flow of packets.
Pros:
  More efficient than Stop-and-Wait ARQ because multiple packets are in transit at the same time.
  Better throughput in high-latency networks.
Cons:
  If a single packet is lost, all subsequent packets need to be retransmitted, even if they were received correctly.
  More buffer space required compared to Stop-and-Wait ARQ.
Use Cases:
  Used in wireless communication (e.g., RLC layer in LTE networks).
  Good for networks where retransmissions are necessary but not too costly.
GO-BACK-N ARQ

## Slide 14
Latency Leaders
SAMPLE IMPLEMENTATION OF GO-BACK-N-WAIT ARQ

## Slide 15
How it Works:
  The sender transmits multiple packets without waiting for an acknowledgment.
  If a packet is lost or corrupted, the receiver requests only that specific packet to be retransmitted (instead of retransmitting all subsequent packets like in Go-Back-N).
  The receiver stores correctly received packets in a buffer and waits for the missing packet to arrive.
Pros:
  More efficient than Go-Back-N because only the lost/corrupted packets are retransmitted.
  Higher throughput as unnecessary retransmissions are avoided.
Cons:
  Requires more complex processing and larger buffer memory at both sender and receiver to handle out-of-order packets.
  Higher overhead due to the need for individual acknowledgments.
Use Cases:
  Used in high-speed and high-latency networks where efficiency is critical (e.g., LTE/5G RLC layer, TCP).
  Satellite and wireless communications where retransmission costs are high.
SELECTIVE REPEAT ARQ

## Slide 16
Latency Leaders
SAMPLE IMPLEMENTATION OF SELECTIVE REPEAT ARQ

## Slide 17
Latency Leaders
COMPARISON BETWEEN ARQ TYPES

## Slide 18
KEY PARAMETERS IN RLC ARQ
Latency Leaders

## Slide 19
  Max Retransmissions: The maximum number of retransmissions allowed for a packet. If the packet is not successfully received within these attempts, the data may be discarded or an error is triggered.
  Window Size: RLC ARQ uses a sliding window mechanism for flow control. It allows the sender to transmit multiple packets without waiting for individual acknowledgments but ensures that the sender doesn't overwhelm the receiver.
  Sequence Number: The sequence number is used to identify each data packet uniquely. It ensures that the receiver can detect packet losses and handle out-of-order packets.

## Slide 20
ERROR HANDLING
Latency Leaders

## Slide 21
If a packet is lost or corrupted during transmission, the receiver cannot decode it correctly. In such cases:
  Negative Acknowledgment (NACK) is sent to inform the sender that retransmission is required.
  The sender will then use the ARQ mechanism to retransmit the lost or corrupted packet.

## Slide 22
Step 1: The sender transmits data packets.
Latency Leaders
RLC ARQ IN ACTION
Step 2: The receiver acknowledges the receipt of the packets (ACK).
Step 4: The sender retransmits the lost packet.
Step 3: If the receiver detects an error (lost or corrupted packet), it sends a NACK.
Step 5: The receiver acknowledges the successful receipt of the retransmitted packet.

## Slide 23
BENEFITS OF RLC ARQ
Latency Leaders

## Slide 24
  Reliability: Ensures that data is transmitted correctly over the wireless link.
  Error Detection and Recovery: Can recover from errors such as lost or corrupted packets.
  Efficiency: The sliding window and ARQ mechanisms help optimize the use of bandwidth and reduce retransmissions, making communication more efficient.

## Slide 25
CHALLENGES
Latency Leaders

## Slide 26
  Delay: Continuous retransmissions can introduce delay, especially in cases of poor signal quality.
  Buffering: Managing buffer space for retransmissions requires additional resources.
  Overhead: The ARQ process adds some overhead due to the need for acknowledgment packets.

## Slide 27
CONCLUSION
Latency Leaders
In summary, the RLC ARQ procedure is essential for maintaining data integrity and reliability in wireless communication systems by using a mechanism for retransmitting lost or corrupted packets and ensuring efficient data transfer.

## Slide 28
FOR YOUR ATTENTION
Latency Leaders
THANK YOU!